Softwaretechnik Projekt WS21/22, Jakob Czekansky

User Manual Assembly
Pick-by-Light

# Introduction

Welcome to the Pick-By-Light system!

The Pick-By-Light System (hereinafter called PBL) is a system to assist you in finding spareparts in multiple rooms and sparepartscontainers in them. To achieve this the PBL provides a graphical user interface on your smartdevice or webbrowser in which you search for a specific sparepart and the compartment, in which the part is stored, will light up.
This project is an open source project and we highly encourage you to build it on your own and modify the hard- or software to your likings. To ensure you are able to do this you will find in this document all relevant information on which parts you need to build it on your own, the technical specifications and how to assemble the PBL.
Some of the parts need to be 3D printed, you can find all necessary 3D printable master files in the git repository.

# Parts List

A list of parts you need to build the PBL on your own. This listing is specified for a single sparepartscontainer with 12 rows and 4 compartments per row. 3D printed parts are marked with „(3DP)“.

ItemNr	Description	Qty.	Length (if needed)
1	Sparepartscontainer	1
2	ESP32 Microcontroller	1
3	Adafruit Flora Smart NeoPixel (or similar)	48
4	(3DP) LED Holding Mechanism	12
5	(3DP) LED Wedges	48
6	(3DP) LED Holding Mechanism Connector	22
7	(3DP) ESP Box	1
8	(3DP) ESP Box Lid	1
9	10mm x 3mm Neodym Magnets	60
10	Acrylic glass sheets 1,5mm thickness (7cm x 14cm) *	24
11	Acrylic glass sheets wedged 1,5mm thickness (7cm x 14cm front, 3cm x 14cm back) *	24
12	Cable 1mm diameter (between LEDs)	108	8cm
13	Cable 1mm diameter (row connectors)	72	3cm
14	JST Male 3 pole	23
15	JST Female 3 pole	24
16	JST Crimpcontacts	72
17	Jumpercable Male (ESP32 connector)	3	10cm

*specific measurements depend on your sparepartscontainer, the acrylic glass sheets need to lay flat underneath each drawer.

# Technical Specifications

The PBL is powered by an ESP32 microcontroller to which the LEDs are connected. One ESP32 corresponds to one sparepartscontainer, multiple ESP32s are connected via WIFI to a single Raspberry Pi which holds the Frontend and Backend software structures.

In the following datasheet only the hardware components of one sparepartscontainer will be discussed.

## Used hardware

Microcontroller: ESP32
LEDs: Adafruit Flora Smart NeoPixel RGB LED v2 (WS2812B controller)

## Wiring Diagram

## Power Consumption

One NeoPixel draws a maximum of 60mA if all color values are at 100%.
One sparepartscontainer with 48 compartments and so 48 LEDs draws a total of 2,9A at 3,3V.

Depending on how many compartments and LEDs you have per sparepartscontainer you can either power the whole system via the ESP32's pins (as shown in the above wiring diagram) or via a seperate powersupply. If you use the latter option make sure the ESP32 and the LEDs are connected to the same GROUND.

To find a suitable powersupply you can calculate the maximum powerconsumption of your sparepartscontainer with following formusla:

60mA x (NumberOfLEDs) = Powerdrawage

The PBL system can only be powered by a maximum of 5V DC.

For further explanation of powerconsumption consult the adafruit website:
https://learn.adafruit.com/adafruit-neopixel-uberguide/powering-neopixels

# Assembly Guide

## Soldering the LEDs

## Installation of LEDs to holding mechanisms

## Assembly and attachment of holding mechanisms to the sparepartscontainer